## Slide 1: EEEE-721: Research Assignment General Purpose Computing on GPUs
Connor Goldberg
9 May 2016

## Slide 2: Agenda
Introduction
Power Efficiency
Password Recovery for RAR Files
Sorting
String Matching
Computer GO Engine
Conclusions

## Slide 3: Introduction
[11]
[12]

## Slide 4: Introduction
Specs
System Clock: 1152 MHz
Effective Memory Clock: 7010 MHz
Available Memory: 12288 MB GDDR5
CUDA Cores: 3072
Power Consumption: ~600 W
[12]

## Slide 5: Introduction
Graphics Processing Unit (GPU)
  Introduced in the 1980s
  Offloads graphics processing from the CPU
General Purpose Computing on Graphics Processing Units (GPGPU)
  High level languages enhanced with APIs (C / C++)
  Compute Unified Device Architecture (CUDA) by NVIDIA
  OpenCL by Khronos (Originally by Apple)
  Substitutes the graphics shader language
  Shaders  Thread processors
Single Instruction Multiple Data (SIMD) Programs
  Many computation stages connected with highly localized data flow
  Kernel – Parallel application consisting of multiple functions
Notes: The main purpose for a long time was graphics processing
  Vertex transforms, lighting/color calculations, etc
Application Programming Interface
CUDA – NVIDIAs API
Data produced by one stage us used in the next
Each stage implemented differently in hardware

## Slide 6: CUDA Model
[1]
Notes: Texture and Constant memory are cached, but read only
Global memory is not cached but R/W

## Slide 7: Power Efficiency
High Performance Computing (HPC)
  Large scale scientific computations
    Thousands of processors, hundreds of hours of computation  Enormous energy usage
  CPU-GPU Processing Element (PE)
    Increasingly popular architecture
    High performance on massively parallel processing / vector computations
  CUDA PE is not only dependent on the hardware components
Challenges and problems
  Single GPU  ~300 W (Smart phone  0.5 ~ 1 W) [6]
  Power cost components (memory, logic, etc.), code
  Efforts made in hardware consideration, but not parallel programming paradigms
Goal:
  Software methodologies  Optimize power via algorithm design and technique
Notes: HPC used at schools or labs for research and experiments alike
CPU-GPU, makes use of both CPU and GPU efficiently to complete a task
CUDA PE also depends on the high level applications and the algorithms
Average smart phone ~0.5 – 1 W power consumption during usage [6]
Goal is to explore the different programming and SW techniques that allow for power savings

## Slide 8: Power Efficiency
SIMD Algorithm Optimization
  Large scale computations
  Repeated operations using an identical structure
  Ex. matrix multiplication 
  Power measured of each hardware component: CPU, GPU, memory, PCI buses
CPU-GPU PE Architecture
  CPU copies data to the GPU (from MM to GPUM)
  CUDA kernel launched by the host CPU
  GPU executes threads in parallel
  Results copied from GPUM to MM
Notes: Highly parallelizable because no dependencies on previous operations
SIMD efficient (multiple indices in the same register)
All hardware blocks used in the SIMD computation are measured
A CPU-GPU PE (processing element) contains several hardware components (CPU + 1 or more GPUs)
Kernel is the program that controls the GPU

## Slide 9: Power Efficiency
[2]
Algorithm Model

## Slide 10: Power Efficiency
Matrix multiplication algorithms
  Algorithm 1
    Only using GPU (CPU free to do other things)
  Algorithm 2
    Matrix partitioned onto 2 GPUs
  Algorithm 3
    Matrix partitioned onto 2 GPUs and 1 CPU thread
Algorithm | CPU Energy (mWh) | Execution Speedup (s) | Kernel Speedup (%) | CPU Speedup (%) | Overall Energy Savings (%)
1 | 55 | - | - | - | -
2 | 47 | 0.55 | 39.7 | 21.4 | 6.17%
3 | 54 | 0.52 | 37.2 | 20.1 | 2.32%
[2]
Notes: Each GPU needs one thread of the CPU to control it
Counter intuitive that more GPUs is more power efficient
  They do consume more power, but the speedup outweighs the power consumption

## Slide 11: Power Efficiency
Power Consumption
[2]
Notes: 2 GPUs has higher power usage, but shorter time

## Slide 12: Power Efficiency
Conclusions
  Big overheads for CUDA programs
    Kernel initialization becomes significant
Optimization
  C functionality to conditionally use the GPU
Notes: Memory copying and kernel startup
This becomes signification compared to the time it takes for small workloads
The C code will only use the GPU if the matrix is smaller than 500 elements

## Slide 13: Password Recovery for RAR Files
Encryption/decryption of RAR files  AES keys
  Most time consuming step in the RAR process
Implemented in CUDA
  Thread creation and scheduling can be ignored
  Memory usage is important
    Global, constant, shared, register
AES-128
  Key and initial AES vector generated by SHA-1 and a password
    Password transformed into Unicode and concatenated with salt
    SHA-1 is performed up to 262144 times to generate the key and vector
  The most time consuming due to number of SHA-1 computations
Notes: RAR is just a specific format for compressed data that can be encrypted with a key
Different types of memory for different uses
User entered password
Salt is randomly generated data

## Slide 14: Password Recovery for RAR Files
Parallelizing
  Each key generation will run on its own thread
  If the loop is too large, the OS will stall
  Large loop divided, saving state between loops
Memory Usage
  Frequently used data  Shared memory (execution resource)
  Must be smart about the memory allocation
  If shared memory increases, thread execution decreases
Notes: SHA-1 state is saved while the kernel calls the loop multiple times
Still the disadvantage of storing the state between kernel calls
Shared memory has quick access times
However shared memory is an execution resource
  If too much is used, fewer threads can be executed simultaneously  performance loss

## Slide 15: Password Recovery for RAR Files
Performance
  Memory optimization
    Shared vs. global
Related work
  Using multiple GPUs for this task
  Using ASICs or FPGAs to accelerate cryptographic algorithms
  SHA-1 and MD5 on GPUs
[3]
Notes: Other hashing algorithms used in crypto

## Slide 16: Parallel Sorting
[8]
Notes: No “best” algorithm, always a catch somewhere whether its worst case, or space complexity
Space complexity is related to physical usage (memory)
This paper compares a parallelized mergesort with the C++ STL Quicksort

## Slide 17: Parallel Sorting
Odd-even merge sort
  Basic problem in computing, but has complexity
  Improved in GPUs through the complete parallelism of each iteration
Previous approaches
  Used shader language on older GPUs
  Had a restriction on the data set: elements
Implemented using OpenCL on an ATI GPU
  Groups of compute units
    Based on SIMD architecture with instructions in VLIW format
  Super light-weighted threads
Notes: High complexity makes it bad in most cases
Shader language – no advanced memory control or special hardware for general purpose computations
Restriction makes it not suitable for real applications

## Slide 18: Parallel Sorting
[9]
Simplified ATI GPU Architecture

## Slide 19: Parallel Sorting
[10]

## Slide 20: Parallel Sorting
Results compared with C++ STL quick sort
  Data generated randomly with a uniform distribution
If is the number of processors:
  Complexity: in practice
[4]
Notes: The # of processors is < doulble, but the speedup is > double!
Speedup increases with data length and also improves with processor count

## Slide 21: String Matching
Locating the appearance of a smaller one-dimensional array (size ) within a larger one (size )
Several algorithms implemented in CUDA:
  Naïve
  Knuth-Morris-Pratt (KMP)
    Prefix algorithm 
    Matching algorithm 
    Overall  (linear time)
  Boyer-Moore-Horspool (BMH)
    Overall  < <
  Quick-Search
    Overall  < <
Notes: Usually a smaller string inside of a larger string (text)
KMP -> left to right
BMH -> right to left
QS -> simplified BMH for short patterns

## Slide 22: String Matching
Speed improvement when using shared memory
[5]

## Slide 23: String Matching
[5]
Run time as compared with the CPU for threads

## Slide 24: String Matching
Results
  Parallel implementation  Up to 24x faster
Future work
  Examine performance on multiple GPUs
  Further optimize the parallel implementation
    Make better use of GPUs capabilities
    Loop unrolling, matrix reordering, smarter shared memory
Notes: Up to 24x when using large text and small pattern sizes (where the GPU becomes better than the CPU)

## Slide 25: Computer GO Engine
[7]
Notes: 18x18 grid

## Slide 26: Computer GO Engine
Using a Monte-Carlo Tree Search targeted for a GPU
  Tree traversal to evaluate board situations
  CPUs fail to have enough computing power to meet the needs for GO’s search space
  Thousands to hundreds of thousands of simulations
  Takes advantage of the L1 Cache on the GPU (shared memory)
Algorithm
  Randomly pick a valid point on the board
  Repeat this until there are no valid points left
  Return the result
Results
  Performance improved greatly compared to CPUs simulations
Notes: Monte-Carlo algorithm, based on random decisions under certain constraints
Even though so many simulations, order does not matter  Parallel!
Need to parallelize to make up for the lack of AI

## Slide 27: Conclusions
GPUs are becoming increasingly popular
  The computer gaming market is driving the GPU production rate
The number of APIs and their ease of use is increasing
  CUDA’s available language bindings:
    C, C++, Java, Lua, MATLAB, C#, Perl, Python, more...
A lot of potential especially with multiple GPUs / CPUs
  The limiting factor is the programming
Notes: Limiting factor on the fundamental understanding/methodology to make parallel programs and how to do it

## Slide 28: Main References
[1] | Q. Zhang and Z. Liu, "A parallel design of computer Go engine on CUDA-enabled GPU," 2011 IEEE International Conference on Cloud Computing and Intelligence Systems, Beijing, 2011, pp. 85-88.
[2] | Da Qi Ren and R. Suda, "Investigation on the power efficiency of multi-core and GPU Processing Element in large scale SIMD computation with CUDA," Green Computing Conference, 2010 International, Chicago, IL, 2010, pp. 309-316.
[3] | G. Hu, J. Ma and B. Huang, "Password Recovery for RAR Files Using CUDA," Dependable, Autonomic and Secure Computing, 2009. DASC '09. Eighth IEEE International Conference on, Chengdu, 2009, pp. 486-490.
[4] | K. Zhang, J. Li, G. Chen and B. Wu, "GPU accelerate parallel Odd-Even merge sort: An OpenCL method," Computer Supported Cooperative Work in Design (CSCWD), 2011 15th International Conference on, Lausanne, 2011, pp. 76-83.
[5] | C. S. Kouzinopoulos and K. G. Margaritis, "String Matching on a Multicore GPU Using CUDA," Informatics, 2009. PCI '09. 13th Panhellenic Conference on, Corfu, 2009, pp. 14-18.

## Slide 29: Other References
[6] | Aaron Carroll and Gernot Heiser. 2010. An analysis of power consumption in a smartphone. InProceedings of the 2010 USENIX conference on USENIX annual technical conference(USENIXATC'10). USENIX Association, Berkeley, CA, USA, 21-21.
[7] | Katpatuka. 2005. Go-board-animated.gif. https://upload.wikimedia.org/wikipedia/commons/f/f3/Go-board-animated.gif
[8] | "Big-O Algorithm Complexity Cheat Sheet", Bigocheatsheet.com, 2016. [Online]. Available: http://bigocheatsheet.com/. [Accessed: 06- May- 2016].
[9] | AMD Corporation. ATI Stream Computing OpenCL Programming Guide, March 2010.
[10] | "VisuAlgo - Sorting (Bubble, Selection, Insertion, Merge, Quick, Counting, Radix)", Visualgo.net, 2016. [Online]. Available: http://visualgo.net/sorting. [Accessed: 06- May- 2016].
[11] | Core0.staticworld.net, 2016. [Online]. Available: http://core0.staticworld.net/images/article/2015/03/geforce_gtx_titanx_3qtr-100573547-orig.png. [Accessed: 06- May- 2016].
[12] | Amazon, 2016. [Online]. Available: http://ecx.images-amazon.com/images/I/61wR4O5hm3L._SL1200_.jpg. [Accessed: 08- May- 2016].